PATH 36 Uniform Protocol for Energy-Efficient Remodeling of Existing Housing

HUD Contract Number C-CHI-00800/CHI-T0001

#### Develop Preliminary Specifications

Task Report

January 2006

Prepared by

Team IBTS

Institute for Building Technology and Safety

Herndon, VA

Responsible IBTS subcontractor:

Performance Systems Development, Inc.

Ithaca, NY

Prepared for

Office of Policy Development and Research

U.S. Department of Housing and Urban Development

Visit PD&R’s Web site

www.huduser.org

to find this report and others sponsored by

HUD’s Office of Policy Development and Research

(PD&R).

Other services of HUD USER, PD&R’s Research and

Information Service, include listservs; special

interest, bimonthly publications (best practices,

significant studies from other sources); access to

public use databases; hotline 1–800–245–2691 for

help accessing the information you need.

The contents of this report are the views of the contractor and do not necessarily reflect the views or policies of the U.S. Department of Housing and Urban Development or the U.S. Government.

Table of Contents

1: Introduction	4

Overview	4

Document Organization	5

Definitions	5

2: Foundations for the Specification Design Process	6

A Multi-Level Protocol	6

Major Task 3 Findings and Conclusions	7

Lessons from the PIER Project	7

3: Protocol Information System Specification	8

Principles for the Protocol Information System Design	8

User Type Specification	9

Level Usage	10

Best Practice Process Specification	13

4: User Interface Specification	14

Data Formats	15

Checklists	15

Customized Documentation	15

User History	16

5: Graphical Specification of the Information System Structure	17

Major Elements of the Information System	17

Best Practice Process Table Specification	18

Organization of Improvements	19

References Specification	22

Appendix A: Sample Improvement Protocol Outline	23

APPENDIX B: Detailed Whole House Improvements Table	30

# 1: Introduction

## Overview

#### This is the final report for the PATH 36/Phase 1 project’s Task 4.1:  “Develop Preliminary Specifications.” This report details the scope of the information delivery model for the PATH 36 Uniform Protocol for energy efficient remodeling, and specifies its requirements.

The report also examines the long-range implications of the protocol information system’s adaptability, maintenance, deployment and suitability for additional audiences such as energy-efficiency programs, educators/trainers, contractor organizations and consumers. It also includes a “specification map” that outlines the organization of the information system.

The ultimate deliverable for this project is a multi-layered information system that remodeling contractors can use to incorporate PATH 36 protocols for energy efficiency into their construction and business practices. The online, interactive system will include a path of increasing complexity that is driven by each contractor’s own best business interests and encouraged by their marketing efforts.  An up-front training component will include basic foundational concepts, for example, the basic principle that air is a fluid.  This concept is critical to understanding how the pressure influences in one part of a house impact the air flows in other parts of a house, most critically the air flows related to combustion appliances.  Early reinforcement of a small group of similar critical concepts, in an easy to understand fashion complete with visualization of the concepts, will assist contractors in understanding why understanding the entire building as a system approach has value.

For success, the design of the information system must include the following key parameters.

1. Filtering Data for End Users. The information system’s target audience includes contractors who work on a variety of housing types in a range of climates. Because of the broad scope of users, the system must filter data so that contractors can retrieve information specific to their interests. As a result, the system will provide a common data structure for its audience that functions on multiple levels.

The information system should introduce contractors to the PATH 36 protocols seamlessly, so they can quickly see the benefits for themselves and their customers, and the advantages of progressing though the information system.

The system must add instant value for users by providing immediately usable, straightforward information. The system should not overwhelm users with information, but give them the option to find more detail by clicking on links.

2. Dynamic Content. In order to address evolving technologies and techniques and new remodeler energy efficiency and home performance programs, the information system must be an adaptable, dynamic reference that is easily maintained and updated, preferably by periodic review and input from participating contractors.

3. Levels. The information system will be organized into three levels. Level 1 will offer an introduction to contractors, focusing more on individual improvements than entire processes. All levels may contain similar topics, but the information on the topic will change with each level.  For example, combustion safety information provided at Level 1 will be very different than the combustion safety information provided at Level 2 or 3.

4. Individual Improvements. The information system should include a section specifically for individual improvements (Energy Conservation Measures). These improvements provide a practical introduction for beginning users, who will likely be more interested in how a specific technology fits into their business than an entire process. The improvements section should include links to best practice processes that guide beginners to learn about processes that result in greater energy efficiency and customer satisfaction. Figure 9 shows the structure of an individual improvement protocol, and Appendix A provides a sample of an example of the Air Sealing Improvement Protocol.

## Document Organization

This report is divided into five sections. Section 1 includes an overview of the report. Section 2 includes background information from previous tasks and projects. Section 3 focuses on the requirements used to develop the specification. Section 4 describes the user interface and the output from the information system.  Section 5 provides a written and visual specification of the data contained in the information system.  The Appendices provide detailed information on improvements.

## Definitions

Contractor: For the purposes of this report the “contractor” generally implies a remodeling contractor. Because contractors are the primary target audience of the information system, the report often uses the term “contractor” interchangeably with “user.”   Further detail on the types of users is provided below under User Type Specification.

Individual Improvement: A specific technology or technique that beginning users can perform. Unlike whole-house improvements performed at higher levels, individual improvements are less intensive and more approachable for beginners.

Information System: The deliverable for the PATH 36 project, an interactive, online database that encompasses all PATH 36 protocols. Information in the system is filtered for each user based on his or her knowledge, experience and contractor type, and the climate and building type for the project. The system is organized into three increasingly complex and beneficial levels. Contractors can progress through the levels as they increase their knowledge and skill.

Protocol: A protocol is a standardized and agreed way to do something. In this report, the term “protocol” indicates one of the energy-efficient remodeling protocols outlined by the PATH 36 project.

User Interface: The screen that the user interacts with while using the information system.

# 2: Foundations for the Specification Design Process

## A Multi-Level Protocol

The information system relies on layered and progressive elements that are organized into three general levels of activity. Each level is more difficult than the one below it, but also provides better energy savings and other rewards.  Tasks at each level will be designed to make contractors feel successful early on, so they have incentive to take the next step.  As contractors master each new task and level, the information system encourages them to progress to higher-level activities.

- Level 1 addresses simple energy-efficiency strategies aimed to improve conventional remodeling approaches.

- Level 2 addresses more systematic home assessments and repairs than Level 1. Contractors at this level begin to diagnose home performance with tests, such as blower door tests.

- Level 3 information is comprehensive and addresses full-scale, whole-house energy retrofit analyses, job bids, installation and quality assurance.

For more detail about how contractors will use each level, see “Level Usage,” p. 10.

Each level will prepare contractors for various types of certification tests. For example, completing Level 2 is roughly equivalent to passing a BPI Core level test, the introductory level of BPI testing. The information system can provide links to various certifications, including North American Technician Excellence (NATE), the Building Performance Institute (BPI), National Association of the Remodeling Industry (NARI), National Association of Home Builders Remodelers Council and others.

## Major Task 3 Findings and Conclusions

The Task 3 industry survey established a baseline of current remodeling practices to provide a foundation for developing a comprehensive scope for the protocol. Some findings included:

- The contracting industry is seriously fragmented.  Small companies with limited capital dominate the market.  These types of companies currently find it difficult or unrewarding to incorporate energy efficiency into their remodeling practices. The information system must provide support and value to contractors who change their business practices to include energy efficiency.

- Testing and diagnostic equipment are rarely used. The protocol must provide a user-friendly path to best practices, starting with a visual assessment that demonstrates the value of diagnostic testing.

- Remodelers generally lack the understanding and capability to offer consumers energy-efficiency improvements.  Education is a critical component of any change, and must be included throughout the information system, from the onset through the deepest level of detail.

- Lack of standardization and understanding building science in the remodeling industry often results in poor installation quality. The information system must provide simple mechanisms that contractors can use to assess and meet minimal standards. It must also include project test-outs that assure quality, but with varying degrees of difficulty, so that newly-initiated contractors are not intimidated by the process.

## Lessons from the PIER Project

The design of the PATH 36 Uniform Protocol provides contractors with a path to whole-house home performance improvements. This was largely defined by the California Energy Commission’s (CEC) Public Interest Energy Research (PIER) project. PSD and BKi completed 40 detailed whole-house protocols. Team IBTS used these protocols to define the initial scope for Level 3.

Information from the PIER project also helped shape Levels 2 and 3, which allowed Team IBTS to work backward from a well defined whole-house approach.

Level 1 protocols are based on existing industry standards. Practices gradually morph from these standards into the PIER-based whole-house protocols at Level 3.

BKi and PSD learned several lessons from developing and implementing the PIER protocols. The PATH 36 protocols and information system will incorporate these lessons in its design. Findings included:

- Information must be structured properly to be useful.  Each user’s specific circumstances will affect their ability to use information. Therefore, the information system must provide only the information contractor needs only when it is needed.

- The target audience is not a community that prefers to get information via reading.  Protocol information must extend beyond text-based guidance. It can address a range learning styles by incorporating video and audio clips, printer-friendly documents and links to other resources.

- The PIER protocols focus heavily on introducing whole-house processes without spotlighting individual improvements that contractors could recommend. Instead, the PATH 36 set should move contractors incrementally toward energy efficiency by encouraging the merits of individual improvements suitable for recommending to customers without a whole-house investigation.

# 3: Protocol Information System Specification

## Principles for the Protocol Information System Design

Team IBTS proposes the following guidelines for designing the information system:

1.	Use strategies and guidelines that support the contactor’s full business and full installation lifecycle. This includes sales, marketing, installation and customer service.

- Many contractors know how to install equipment, but don’t know how to sell it. Yet selling is vital to success with energy efficiency; without effective sales and marketing approaches, remodelers will not be able to sell energy-efficient remodeling projects.

- Without installation guidelines, projects are not completed correctly and do not produce the desired result for the customers or the contractors.

- Contractors that quickly learn sales and marketing techniques will have more success adopting EE protocols.  It is anticipated that contractors will not start talking about home performance unless they can answer typical questions.   We need to do a good job of preparing them with talking points and training.

2.	The protocols must reduce, not increase contractor liability.

- In the PIER project and in home performance, diagnostic test-in, test-out testing is used to limit contractor liability. But testing may not be a feasible Level 1 activity, which means that other methods for reducing liability are necessary.

3.	The system must give contractors an adaptable set of pricing criteria that allows them to accurately price the proposed improvements under a variety of existing conditions.

- The project may be linked with national remodeler and HVAC pricing guides to include recommended energy-efficiency improvements in their guides.

4.	Contractors need to know what to evaluate in a building in order to offer improvements. Therefore, the contractor’s data collection process must include screening for improvements.

- Collecting the right data before pricing the job is critical. Excluding key installation variables can cause a job to lose money.

- The contractor’s data collection should include improvements to recommend to the customer. Contractors who want to propose an improvement need to collect enough data to accurately price it and estimate its potential savings.

- Most contractors have a standard sales process that works for them. The protocol set should build on their existing system, rather than replace it. A contractor can’t collect all the data for all possible improvements, the system must define and allow for properly focused data collection that will add obvious value to the contractor’s proposal.

- In general comprehensive data collection is not appropriate for Levels 1 and 2. The information system must strike a balance between too much and too little information.

5.	Rapidly filtered and customized information will increase the value of the system for users.

- The IBTS team will understand the needs and limitations of contractors. This understanding will guide the design of the system. In turn, contractor needs will guide the information they access.

- The faster the system can direct contractors to useful information the more contractors will use the system.

6.	The information system must include links to consumer awareness efforts to create market pull.

- Any marketing support that the information system offers must be tied in to the consumer outreach efforts of other organizations, such as BPI, ENERGY STAR and NARI.

7.	The design must include provisions for protocol maintenance.

- The remodeling and home performance industries need a comprehensive set of energy-efficiency and home performance best practices that is widely accepted across multiple organizations in the industry. To accomplish this, a foundation of standard practices needs to be reviewed and adopted collaboratively by contractors and stakeholders nationwide. Eventually, this collaboration should evolve into a permanent process. The American Society of Refrigerating and Air-Conditioning Engineers (ASHRAE) offers an example of how this process could work.

- The information at the core of the database also requires maintenance, preferably an ongoing, industry-based system of proposing, reviewing and accepting new information and changes.

- A customizable database will support development of local or regional funded energy-efficiency programs. Because funded programs seek to develop best practice guides that are customized to the specific design of their program, they would not be able to use a fixed set of protocols.

## User Type Specification

The system will be built to be accessible to a wide range of contractors.  Initially, we will target contractors with technical skills and an interest in learning - and then expand the system to reach out to contractors with fewer technical skills.  This will create early successes for the system and we can then expand our focus accordingly.  The information system will plan for a range of user types, including:

- Consultative Sales: These contractors provide consultative sales for big jobs with long gestations. They are generally local non-franchise home remodelers, and their sales process is expensive and time consuming.

- Specialty sales: These users include kitchen, deck or windows specialists who perform moderate to big jobs. Their businesses incorporate a fairly quick and professional sales process and standardized processes. They are often chains/franchises and are mass-marketing-based.

- Repair / Replacement: These contractors repair and/or replace individual components, such as HVAC roof, paint and drainage. They can be small and local or large national chains, such as SEARS, and are highly price competitive. Their businesses offer a very limited scope, with an emphasis on quick sales and fast installation.

- Educator/Trainer:  These are experienced contractors or professional educators who provide training services, either as private contractors or as part of educational institutions.

- Homeowner: Although homeowner “do-it-yourselfers” are not a target audience of the protocol, the system should prepare for their use.

In order to keep the information system up-to-date, it requires regular maintenance and should employ three distinct positions:

- Topic Reviewer: Reviewers have tactical expertise in a specific topic. Each will act as part of a group to provide input on content suitability for that topic.

- Topic Manager: Like reviewers, managers are also experts on a specific topic. They will manage all content at that topic level.

- Program Administrator: The administrator develops individual programs and manages variations in the database.

## Level Usage

The following examples explore what a remodeling contractor will find at each level of the PATH 36 information system.  There is a suggested starting point for each level, creating a suggested linear list of topics within a level.  We are attempting to offer “training wheels” as opposed to a full-cycle business system.  The levels start out being very easy to understand and easy to adopt, and then move to more difficult practices.  The change in level occurs with more significant expectations in the change in business process.

Level 1:

Level 1 contractors must have an internet connection, an interest in learning about energy efficiency and adequate selling skills. Do-it-yourselfer homeowners will use this level.

Contractors at this level can use the PATH 36 website to identify improvements for a job before estimating it, and to print out visual walkthroughs that are customized for the building type, climate type and contractor type. Once the contractor has used the walkthrough to collect information about the building, the website recommends simple improvements, such as providing ENERGY STAR appliances, performing air sealing and installing proper insulation, as well as additional improvements, such as basic attic sealing and assessing the potential for combustion backdrafting.

The contractor can use the website to help decide how to implement these improvements and to determine pricing.  For example:

- If the contractor identifies air leakage sites in the attic, he can access the protocol documents to decide how to treat the sites and develop a price.

- The contractor can include the air sealing in their estimate for a kitchen remodeling job since he will be in the attic anyway when running new wiring. He can explain to the client how these simple improvements will improve the overall comfort and energy efficiency of the home.

- If the contractor finds visual evidence of combustion problems such that home testing is necessary, the website provides links for contacting NATE certified contractors, HERS raters, or BPI-certified contractors and guidance for working with them.  Home performance contractors can use a website-provided protocol when testing the home.

Level 2:

After completing Level 1, contractors move away from individual improvement opportunities toward a diagnosis process. Level 2 includes an introductory diagnosis process that is driven by performance testing. This process can be conducted with external testing contractors, or contractors can experiment internally with blower door tests or duct testers. Contractors also begin to integrate combustion safety tests.

Level 3:

Level 3 equips users with the business and technical knowledge to be successful whole-house contractors and accredited BPI contractors (or the equivalent). It also supports the contractor’s ongoing learning process beyond simple certification. In addition to the knowledge required by BPI, Level 3 also provides contractors with additional technical information and advice on enhancing business practices.  Level 3 contractors typically make a long-term career commitment to building science.

Level Access. Contractors visit the PATH 36 website to access the information system. They enter the system by providing information that filters the database for their needs and level of knowledge. As their knowledge increases, contractors are promoted to higher levels. Individual protocols vary with the contractor’s operating level. As levels increase, so does the focus on performance testing and a whole-house process.

Figure 1 shows how contractors access the system’s three levels and Figure 2 compares the benefits of the three levels.  Protocols can be presented to the user by economic rank or other mechanisms.

Figure 1. Accessing the Information System

Figure 2. Comparison of Levels.

## Best Practice Process Specification

The best practice process, as described in the Task 3 report, builds upon the process developed for the PIER project. As part of Task 3, the IBTS team expanded the PIER database of building science references and transferred it to this process structure (see Figure 3).  Each of the structure’s cells vary for each of the three levels and by contractor, climate and building type.

Figure 3. Process Structure

# 4: User Interface Specification

The information system’s user interface should consist of an interactive system that is customized to each user’s interests, skills and abilities.  Branching logic may be used to determine correct solutions (or options) based on answers to questions about specific projects.  The user-friendly interface will require contractors to provide basic information on their business model, and will determine the contractor’s knowledge of energy efficiency and performance testing in order to place them in the appropriate level.

As a result, the entry point for an HVAC contractor will look different than the entry point for a remodeling contractor. The customized interface will define the each contractor accesses data and the content they receive.  A brief and voluntary registration allows users to avoid re-entering their characterization information on subsequent visits.

As part of the quick one-time collection of user profile information, content will be presented based on the several categories, including:

- Contractor type

- Climate type

- Level of knowledge determined through basic testing (optional)

- Interest in green strategies

- General data

- Interest in specific improvements

- Marketing type

- Building characteristics (varies by project, not based on initial registration)

The screen mockups in Figure 4 demonstrate how this information could be collected quickly as part of a registration process and optional pretest.

Figure 4. Screen Mockups

## Data Formats

By providing information in several different ways, the Information System can address various needs and learning styles, thereby increasing its value. Data formats should include:

- Video clips to demonstrate complex hands-on activities

- Audio clips to explain concepts and procedural detail

- Printer-friendly or hard copy documentation available when necessary.

- Links to external websites for additional study

- HTML format for convenience

- Courseware for matching data to needs and for tracking progress.

## Checklists

The information system will provide users with checklists to help them stay organized and to provide a measure of quality assurance.  The checklists will be customized to the contractor’s requirements and can be used in paper, computer or PDA-based formats.

For example, a crew could use a checklist to check their work on an attic insulation project. The checklist would verify the insulation reaches all portions of the attic, and that the crew had inspected the basement for bypasses directly to the attic, completed a fire-safety check on the chimney, and cleaned the jobsite. For higher levels, the checklist could include a blower door test and infrared scan to verify performance. A customized checklist might also include improvements recommended by return on investment.

## Customized Documentation

Data retrieved from the Information System will be available online, but users may also want to export the information to paper. For example, they may use the data to train in the field or present it in a proposal or contract. Paper documents produced by the database will be editable as Rich Text Format files (.rtf) that contractors can customize for their business.

Checklists will also be available through personal digital assistants (PDAs), which will provide instant, portable access to all levels of information and use software to track the user’s progress.  For example, contractors can click once the checklist title to get the scope of the task, and double-click on it to get a list of tools and materials.  Clicking once on a step provides detailed guidance for that step, and clicking once on the detail provides a list of linked references to training resources and associated standards (see Figure 5). Information is presented in a variety of data types depending on the complexity of each step.

Figure 5. PDA Checklist

## User History

The Information System is designed for users to return repeatedly for additional information.  A registration system keeps track of the contractor’s progress and activity as part of their user profile.  Contractors can stop using the System at any time, and have the option to return to the exact spot at which they stopped, or return to any point in their user history. PATH can also use this information evaluate how contractors are using the System in order to improve the performance of the interface.

The user history includes an option to enter the address for “current” individual building.  This allows the system to suggest information relating to regionally or nationally available tax incentives, financing, or rebates from utility or state programs.  Address and building type information is passed to a database of incentives.  This information can also be factored into economic calculations.

# 5: Graphical Specification of the Information System Structure

## Major Elements of the Information System

Figure 6 displays how the major elements of the Information System interact with each other. Figures 7 and 8 provide detailed specifications for the major elements in the system.

Once the Information System has filtered information according to the user’s registration information and history, contractors can either explore more topical improvement-centered information or they can begin to change their business model with best practice process-centered information. Both information tables are linked to each other and draw from a common set of references. And both information tables offer contractors relevant reports and resources.

Figure 6. Major Elements of the Information System

## Best Practice Process Table Specification

The best practice process specification is an extension of the structure used in the PIER materials. This specification includes the following components:

- Background: Additional detail for a particular topic, including topic description, scope, tools and materials, history, certification criteria, time standards and location.

- Procedure: Best practices arranged in construction sequence, and supported with a step-by-step description of the process.

- Presentation: Training materials based on a slide presentation with notes.

- Content Variation: The recommendations vary with each level and could be customized by an energy efficiency program.

Figure 7. Best Practice Process Specification Table

## Organization of Improvements

The information system must include both whole-house improvements and individual improvements information system to include individual improvements.

As explained in “Lessons from the PIER Project (p. 7), Level 1 contractors can more easily incorporate information by an individual improvement than by integrating an entire process. Therefore, the information system should start from a reference database of all potential improvements. Each improvement will be linked to the related process issues in the database, ensuring that contractors have all the information they need for safety and success.

The major elements in an improvement are:

- Where do you improve? This section describes the area of the house that will be improved or the potential to upgrade a change already being made to the house.

- What do you improve? This section describes specific objects that may exist in different areas of the house that could be improved.

- How do you improve? This section describes the materials and techniques used to make the improvement, including installation standards.

- How do you diagnose, price, and sell the improvement? This section describes the assessment process before installation.

- Maximizing benefits:  This section provides guidance on how to get the most impact out of the improvement.

- Risks:  This section supports minimizing the risks associated both inaction (not doing the improvement) and action (making the improvement).

- Quality assurance: This section demonstrates how to inspect the quality of an installation.

- Links: This section provides links to both outside information sources and sources within the Information System.

- Other resources: This section describes the variety of available supporting resources.

Figure 8 shows the structure of an individual improvement, and Appendix A provides an outline example of the Air Sealing Improvement Protocol.

Figure 8. Structure of an Individual Improvement

In Levels 2 and 3 contractors move away from individual improvements toward a whole-house approach. Figure 9 outlines whole-house improvements, which are divided by five main branches: Envelope, Energy Inputs, IEQ, Resource Efficiency and Systems. These main branches are further divided by topic. Appendix B provides an improvements specification table that details all of the potential interaction points between the contractor and the building. Contractors may select one or more of these potential improvements and group them so that they are bundled in a proposal. This will optimize the material list and specification as the contractor selects these improvements for a single job.

Figure 9. Whole-House Improvements Table

## References Specification

Figure 10 shows the organization of the references in the information system. The structure includes five main branches:

- Best practices – This is the basic element developed for the PIER project.  Best practices are grouped into what in the PIER document was described as a protocol or and is described here as a “process elements”.  The term protocol is used here to describe the entire system and process elements used to describe the steps in a process.  This table is described above.

- Improvements – This is the link into the Improvements table described above.

- Problems – A list of problems in buildings will be maintained and linked to related references, improvements and process elements.

- Content variation – The default content can vary by a range of user-defined inputs.  Some defaults are assumed and variation stored as needed.

- Reference – This links all the tables to internal and external sources of information.

Figure 10. The References Database Structure

# Appendix A: Sample Improvement Protocol Outline

Air Sealing Improvement Specification

1 Where do you improve?

House Locations

Attic

Finished

Unfinished

Walls

To outside

To attics

To garages and porches

Basement

Stone

Concrete

Block

Other

Garage

Attached

Separate

Crawlspace

Sealed

Vented

Windows

Basement

Finished space

Doors

Basement

Finished space

Doors to attics

Upgrade options

Room remodel

Whole house remodel

What do you improve?

Specific Objects

Electrical

Plumbing

Windows

Ducts

Heating Pipes

Sill

Attic hatch

Whole house fan

Other

Recessed lights

Chimney Chase

Plumbing chase

Outlets

Switch plates

How do you improve?

Materials and Techniques

Strategic dense pack cellulose

Installation standards

Foam

Installation standards

Caulk

Installation standards

Insulation boards and metal

Installation standards

Plate covers

Installation standards

Weatherstripping

Installation standards

How do you diagnose, price and sell the improvement?

General base building data

CFM50 test

Visual alternative

Dimension

Zone type

Creating improvement

Savings estimate

Changed by improvement

Post CFM 50 Estimated

What materials are needed and quantity

Cellulose

Tubes of caulk

Foam

One part

Two part

Weatherstrip

Insulation board

Plate covers

Other

Detailed installer data influencing price

Location and Number of locations for air sealing

Access

Head clearance

Framing layout

Ventilation required

Electrical

Knob and tube

Incentives available

Tax

Rebates

Financing terms

Installer data collection not influencing price

Notes

Photos

Quality assurance

Visual Checklist

Performance tests

Links

To related best practice procedure sections

Blower door testing

Combustion safety

Subtopic

Visual inspection of the building envelope

To outside sources of information

Home Energy Articles

DOE

PATH

EPA Home Sealing info

Other Resources

Videos

Checklists

Audio

Forms

# APPENDIX B: Detailed Whole House Improvements Table

- Energy Inputs

Fuel choices

Natural gas

Electricity

Oil

Propane

Wood

Coal

Renewable

Types

Solar electric

Roof mount

Ground mount

Solar thermal

Space heating

Hot water

Wind

Site

Orientation

Exposure

Average wind speed

Shading

Installations

Interconnect

Inverter

Net metering

Storage

Batteries

Tanks

Rate changes

Electricity

Submetering

Demand metering

Load control

Change supplier

Green supplier

Gas

Wholesale purchase

Oil

Contracts

Propane

Resource Efficiency

Waste reduction

Materials selection

Systems

Furnace

Detail

Equipment

Clean

Replace

Equipment types

Repair

Blower

Replace

ECM

Motor controller

Clean

Ducts

Treatment

Repair

Seal

Mastic

Polybuytlene tape

Replace

Insulate

Fiberglass wrap

Foam

Bury with cellulose

Duct Type

Supply

Return

Delivery

Grilles

Registers

Named Improvements

Install new furnace

Distribution System Repair

Distribution System replace

General Data

Location

Equipment repair or clean and tune

Misc

Boiler

Detail

Equipment

Replace

Munchkin

Repair

Clean and tune

Piping

Insulate

Replace

Pumps

Replace

Repair

Radiation

Convectors

Baseboard

Radiators

Radiant heat

Named Improvement

Install new boiler

Repair boiler

Cooling

Detail

Equipment

Bryant

Ducts

Return

Repair

Seal

Replace

Insulate

Supply

Repair

Seal

Replace

Insulate

Controls

Thermostat

Programmable

TXV

Refrigerant

Alternate Refrigerants

Blower

ECM

Clean

Delivery

Grilles

Registers

Named Improvement

install cooling system

Repair cooling system

Geothermal

Detail

Water to air

Water to Water

Loop type

Horizontal

Vertical

Named Improvement

Temperature Controls

Detail

Thermostat

Programmable

Remote control

Demand control

Named Improvement

Mechanical Ventilation

Equipment

Bath fan

Kitchen fan

Central exhaust

Air to Air Heat Exchanger

ERV

HRV

Ducts

Repair

Replace

Install

Controls

Humidistat

Timer

On demand override

DHW

Equipment

Replace

Tank

Natural draft

Brands and Models

Natural draft sealed

Brands and Models

Indirect fired

Brands and Models

Power draft

Brands and Models

Tankless

Brands and Models

Solar

Brands and Models

Insulate

Change settings

Pipes

Insulate

Replace

Recirculation

Controls

Pumps

Water use reduction

Manifolds

Pump back systems

End uses

Replace showerheads

Replace faucet aerators

Leaks

Repair

Lighting

Treatment

Replace Bulbs

Replace Fixtures

Area

Inside

Outside

Appliances

Refrigerator

Replace

Brands

Clean coils

Freezer

Replace and recycle

Brand

Clean coils

Remove and Recycle

Washer

Horizontal axis

Brand

Dryer

Fuel change

Kitchen

Microwave

Dishwasher

Entertainment

Reduce vampire losses

Waterbeds

Replace with mattress

Insulate

Water Pumps

Replace pressure tank

Computers

Sleep settings

LCD monitors

Water

Toilets

Leaks

Irrigation system repair

IEQ

Radon

Remediation

Testing

Isolation

Dust

Filters

Electrostatic

Media Filter

Central Vacuum

HEPA floor vacuum

Mold

Removal and cleaning

UV light

VOCs

Removal

Venting

Lead

Control strategies

Remediation

Fire Hazard

Removal

Repair

Detector installation

Asbestos

Control strategies

Remediation

CO and Venting

Venting repair

DHW Orphan

DHW vent

Heating vent

Space heater vent

Replacement of appliance

Seal ducts

Fireplace repair

Pointing

Liner

Chimney repair

Pointing

Liner

Cleaning

Appliance clean and tune

Oven

Burner

Detector installation

Mechanical room

Living area

Garage

Moisture Control

Exterior grading

Gutters

Cleaned

Repaired

Replaced

Installed

Drainage improvements

Roof flashing

Roof repair

Window flashing

Sump pumps

Ground vapor barrier

Irrigation system repair

Roof ventilation

Ridge vent

Mushroom vent

Gable vent

Vent dryer

Vent exhaust fan

Vent recirculating kitchen vent

Dehumidistats

Envelope

Air Sealing

Area

Attic

Finished

Unfinished

Walls

To outside

To attics

To garages and porches

Basement

Stone

Concrete

Block

Other

Garage

Attached

Separate

Crawlspace

Sealed

Vented

Windows

Basement

Finished space

Doors

Basement

Finished space

Doors to attics

Penetrations

Electrical

Plumbing

Windows

Ducts

Heating Pipes

Sill

Attic hatch

Whole house fan

Other

Recessed lights

Chimney Chase

Plumbing chase

Outlets

Switch plates

Penetrations

Electrical

Plumbing

Windows

Ducts

Heating Pipes

Sill

Attic hatch

Whole house fan

Other

Recessed lights

Chimney Chase

Plumbing chase

Outlets

Switch plates

Treatments

Strategic dense pack cellulose

Foam

Caulk

Insulation boards and metal

Plate covers

Weatherstripping

Named Improvement

General air sealing

Insulation

Areas

Attics

Floor

Ceiling

Slope

Hatch or door

Walls

Plank

Brick

Tongue and groove

Stucco

Cedar shingle

Vinyl siding

Asbestos shingle

Floors

To basement

To crawlspace

To garage

Basement

Crawlspace

Other

Roof

Treatments

Cellulose

Spray

Dense pack

Open blow

Dense pack with cover

Foam

Spray

Board

Fiberglass

Batt

Sheet

Board

Named Improvements

Wall insulation

Attic Insulation

Basement wall

Floor

Crawlspace

roof

Windows and doors

Replacement Inserts

Brand

Full replacements

Brands

Interior storm

Brand

Replacement door

Repair

Caulk

Window Hardware

Door hardware

Door frame

Glass

Trim

Materials

Glass

Layers

Two

Three

Treatments

Low e

Low e high SHGC

Other

Gas

Air

Argon

Krypton

Spacer

Warm

?

Frame

Wood

Vinyl

Aluminum

Fiberglass

Named Improvements

Window replacement

Door Replacement

Window repair

Door repair

Roof

Repair

Moisture control

Foundation

Repair

Moisture control

# Text boxes

Levels of Refinement

2

3

1

Topics of Home Improvement

Remodeling Contractor Types

Broader and Harder…But More Energy Savings Plus Other Benefits

Easy, Some Energy Savings

Fewer Contractors

Many Contractors

- Reduced liability insurance

- Maximum energy savings and benefits

- Home Performance with Energy Star

- BPI certification and accreditation

Hardest, Most Comprehensive…BUT

HVAC

Remodeler

Other